## Slide 1: Topic 2 LAN Switching Technologies
CCNA Routing and Switching
200-120 Examination
Jeng-Yueng Chen
Hsiuping University of Science and Technology

## Slide 2: 028
Refer to the exhibit. Switch port FastEthernet 0/24 on ALSwitch1 will be used to create an IEEE 802.1Q-compliant trunk to another switch. Based on the output shown, what is the reason the trunk does not form, even though the proper cabling has been attached?

## Slide 3: 028
  VLANs have not been created yet.
  An IP address must be configured for the port.
  The port is currently configured for access mode.
  The correct encapsulation type has not been configured.
  The “no shutdown” command has not been entered for the port.

## Slide 4: 029
Which port state is introduced by Rapid-PVST?
  learning
  listening
  discarding
  forwarding

## Slide 5: 030
VLAN 3 is not yet configured on your switch. What happens if you set the switchport access vlan 3 command in interface configuration mode?
  The command is rejected.
  The port turns amber.
  The command is accepted and the respective VLAN is added to vlan.dat.
  The command is accepted and you must configure the VLAN manually

## Slide 6: 031
What value is primarily used to determine which port becomes the root port on each nonroot switch in a spanning-tree topology?
  path cost
  lowest port MAC address
  VTP revision number
  highest port priority number
  port priority number and MAC address

## Slide 7: 032
In a switched environment, what does the IEEE 802.1Q standard describe?
  the operation of VTP
  a method of VLAN trunking
  an approach to wireless LAN communication
  the process for root bridge selection
  VLAN pruning

## Slide 8: 033
Refer to the exhibit. Switch-1 needs to send data to a host with a MAC address of 00b0.d056.efa4. What will Switch-1 do with this data?

## Slide 9: 033
  Switch-1 will drop the data because it does not have an entry for that MAC address.
  Switch-1 will flood the data out all of its ports except the port from which the data originated.
  Switch-1 will send an ARP request out all its ports except the port from which the data originated.
  Switch-1 will forward the data to its default gateway.

## Slide 10: 034
What is the function of the command switchport trunk native vlan 999 on a Cisco Catalyst switch?
  It creates a VLAN 999 interface.
  It designates VLAN 999 for untagged traffic.
  It blocks VLAN 999 traffic from passing on the trunk.
  It designates VLAN 999 as the default for all unknown tagged traffic.

## Slide 11: 035
Which two protocols are used by bridges and/or switches to prevent loops in a layer 2 network? (Choose two.)
  802.1d
  VTP
  802.1q
  STP
  SAP
802.1d: STP
802.1s: MST
802.1w: RSTP

## Slide 12: 036
Which switch would STP choose to become the root bridge in the selection process?
  32768: 11-22-33-44-55-66
  32768: 22-33-44-55-66-77
  32769: 11-22-33-44-55-65
  32769: 22-33-44-55-66-78

## Slide 13: 037
A switch is configured with all ports assigned to VLAN 2 with full duplex FastEthernet to segment existing departmental traffic. What is the effect of adding switch ports to a new VLAN on the switch?
  More collision domains will be created.
  IP address utilization will be more efficient.
  More bandwidth will be required than was needed previously.
  An additional broadcast domain will be created.

## Slide 14: 038
What are three benefits of implementing VLANs? (Choose three.)
  A higher level of network security can be reached by separating sensitive data traffic from other network traffic.
  A more efficient use of bandwidth can be achieved allowing many physical groups to use the same network infrastructure.
  A more efficient use of bandwidth can be achieved allowing many logical networks to use the same network infrastructure.
  Broadcast storms can be mitigated by increasing the number of broadcast domains, thus reducing their size.
  Broadcast storms can be mitigated by decreasing the number of broadcast domains, thus increasing their size.
  VLANs make it easier for IT staff to configure new logical groups, because the VLANs all belong to the same broadcast domain.
  Port-based VLANs increase switch-port use efficiency, thanks to 802.1Q trunks.

## Slide 15: 039
Which IEEE standard protocol is initiated as a result of successful DTP completion in a switch over Fast Ethernet?
  802.3ad
  802.1w
  802.1D
  802.1Q
802.3ad  Link Aggregation
802.1w  RSTP
802.1d  STP
802.1q  VLAN Tagging
Notes: 802.3ad  Link Aggregation

## Slide 16: 040
Which of the following are benefits of VLANs? (Choose three.)
  They increase the size of collision domains.
  They allow logical grouping of users by function.
  They can enhance network security.
  They increase the size of broadcast domains while decreasing the number of collision domains.
  They increase the number of broadcast domains while decreasing the size of the broadcast domains.
  They simplify switch administration

## Slide 17: 041
Refer to the exhibit. A technician has installed SwitchB and needs to configure it for remote access from the management workstation connected to SwitchA. Which set of commands is required to accomplish this task?

## Slide 18: 041
  SwitchB(config)# interface FastEthernet 0/1
  SwitchB(config-if)# ip address
  192.168.8.252 255.255.255.0
  SwitchB(config-if)# no shutdown
  SwitchB(config)# interface vlan 1
  SwitchB(config-if)# ip address
  192.168.8.252 255.255.255.0
  SwitchB(config-if)# ip default-gateway
  192.168.8.254 255.255.255.0
  SwitchB(config-if)# no shutdown
  SwitchB(config)# ip default-gateway 192.168.8.254
  SwitchB(config)# interface vlan 1
  SwitchB(config-if)# ip address
  192.168.8.252 255.255.255.0
  SwitchB(config-if)# no shutdown
  SwitchB(config)# ip default-network 192.168.8.254
  SwitchB(config)# interface vlan 1
  SwitchB(config-if)# ip address
  192.168.8.252 255.255.255.0
  SwitchB(config-if)# no shutdown
  SwitchB(config)# ip route 192.168.8.254 255.255.255.0
  SwitchB(config)# interface
  FastEthernet 0/1
  SwitchB(config-if)# ip address
  192.168.8.252 255.255.255.0
  SwitchB(config-if)# no shutdown

## Slide 19: 042
Which two states are the port states when RSTP has converged? (Choose two.)
  discarding
  listening
  learning
  forwarding
  disabled

## Slide 20: 043
Which two commands can be used to verify a trunk link configuration status on a given Cisco switch interface? (Choose two.)
  show interface trunk
  show interface interface
  show ip interface brief
  show interface vlan
  show interface switchport

## Slide 21: 044
Which command enables RSTP on a switch?
  spanning-tree uplinkfast
  spanning-tree mode rapid-pvst
  spanning-tree backbonefast
  spanning-tree mode mst

## Slide 22: 045
Refer to the exhibit. All switch ports are assigned to the correct VLANs, but none of the hosts connected to SwitchA can communicate with hosts in the same VLAN connected to SwitchB. Based on the output shown, what is the most likely problem?

## Slide 23: 045
  The access link needs to be configured in multiple VLANs.
  The link between the switches is configured in the wrong VLAN.
  The link between the switches needs to be configured as a trunk.
  VTP is not configured to carry VLAN information between the switches.
  Switch IP addresses must be configured in order for traffic to be forwarded between the switches

## Slide 24: 046
Refer to the exhibit. Which WAN protocol is being used?
  ATM
  HDLC
  Frame Relay
  PPP

## Slide 25: 047
Refer to the exhibit. Given the output shown from this Cisco Catalyst 2950, what is the reason that interface FastEthernet 0/10 is not the root port for VLAN 2?
  This switch has more than one interface connected to the root network segment in VLAN 2.
  This switch is running RSTP while the elected designated switch is running 802.1d Spanning Tree.
  This switch interface has a higher path cost to the root bridge than another in the topology.
  This switch has a lower bridge ID for VLAN 2 than the elected designated switch

## Slide 26: 048
Why will a switch never learn a broadcast address?
  Broadcasts only use network layer addressing.
  A broadcast frame is never forwarded by a switch.
  A broadcast address will never be the source address of a frame.
  Broadcast addresses use an incorrect format for the switching table.
  Broadcast frames are never sent to switches.

## Slide 27: 049
Refer to the exhibit. Why has this switch not been elected the root bridge for VLAN1?

## Slide 28: 049
  It has more than one interface that is connected to the root network segment.
  It is running RSTP while the elected root bridge is running 802.1d spanning tree
  It has a higher MAC address than the elected root bridge.
  It has a higher bridge ID than the elected root bridge.

## Slide 29: 050
Which two link protocols are used to carry multiple VLANs over a single link? (Choose two.)
  VTP
  802.1q
  IGP
  ISL
  802.3u

## Slide 30: 051
Assuming the default switch configuration, which VLAN range can be added, modified, and removed on a Cisco switch?
  1 through 1001
  2 through 1001
  1 through 1002
  2 through 1005

## Slide 31: 052
Which statement about VLAN operation on Cisco Catalyst switches is true?
  When a packet is received from an 802.1Q trunk, the VLAN ID can be determined from the source MAC address and the MAC address table
  Unknown unicast frames are retransmitted only to the ports that belong to the same VLAN.
  Broadcast and multicast frames are retransmitted to ports that are configured on different VLAN.
  Ports between switches should be configured in access mode so that VLANs can span across the ports.

## Slide 32: 053
Refer to the topology shown in the exhibit. Which ports will be STP designated ports if all the links are operating at the same bandwidth? (Choose three.)
  Switch A - Fa0/0
  Switch A - Fa0/1
  Switch B - Fa0/0
  Switch B - Fa0/1
  Switch C - Fa0/0
  Switch C - Fa0/1

## Slide 33: 054
Refer to the exhibit. How should the FastEthernet0/1 ports on the 2950 model switches that are shown in the exhibit be configured to allow connectivity between all devices?

## Slide 34: 054
  The ports only need to be connected by a crossover cable.
  SwitchX(config)# interface fastethernet 0/1
  SwitchX(config-if)# switchport mode trunk
  SwitchX(config)# interface fastethernet 0/1
  SwitchX(config-if)# switchport mode access
  SwitchX(config-if)# switchport access vlan 1
  SwitchX(config)# interface fastethernet 0/1
  SwitchX(config-if)# switchport mode trunk
  SwitchX(config-if)# switchport trunk vlan 1
  SwitchX(config-if)# switchport trunk vlan 10
  SwitchX(config-if)# switchport trunk vlan 20

## Slide 35: 055
Refer to the exhibit. A frame on VLAN 1 on switch S1 is sent to switch S2 where the frame is received on VLAN 2. What causes this behavior?

## Slide 36: 055
  trunk mode mismatches
  allowing only VLAN 2 on the destination
  native VLAN mismatches
  VLANs that do not correspond to a unique IP subnet

## Slide 37: 056
Which three statements about RSTP are true? (Choose three.)
  RSTP significantly reduces topology reconverging time after a link failure.
  RSTP expands the STP port roles by adding the alternate and backup roles.
  RSTP port states are blocking, discarding, learning, or forwarding.
  RSTP provides a faster transition to the forwarding state on point-to-point links than STP does.
  RSTP also uses the STP proposal-agreement sequence.
  RSTP uses the same timer-based process as STP on point-to-point links

## Slide 38: 057
At which layer of the OSI model is RSTP used to prevent loops?
  physical
  data link
  network
  transport

## Slide 39: 058
What does a Layer 2 switch use to decide where to forward a received frame?
  source MAC address
  source IP address
  source switch port
  destination IP address
  destination port address
  destination MAC address

## Slide 40: 059
Refer to the exhibit. Which statement is true?
  The Fa0/11 role confirms that SwitchA is the root bridge for VLAN 20.
  VLAN 20 is running the Per VLAN Spanning Tree Protocol.
  The MAC address of the root bridge is 0017.596d.1580.
  SwitchA is not the root bridge, because not all of the interface roles are designated

## Slide 41: 060
Which two benefits are provided by creating VLANs? (Choose two.)
  added security
  dedicated bandwidth
  provides segmentation
  allows switches to route traffic between subinterfaces
  contains collisions

## Slide 42: 061
Which command can be used from a PC to verify the connectivity between hosts that connect through a switch in the same LAN?
  ping address
  tracert address
  traceroute address
  arp address

## Slide 43: 062
Based on the network shown in the graphic. Which option contains both the potential networking problem and the protocol or setting that should be used to prevent the problem?
  routing loops, hold down timers
  switching loops, split horizon
  routing loops, split horizon
  switching loops, VTP
  routing loops, STP
  switching loops, STP

## Slide 44: 063
Refer to the exhibit. Which two statements are true about interVLAN routing in the topology that is shown in the exhibit? (Choose two.)

## Slide 45: 063
  Host E and host F use the same IP gateway address.
  Router1 and Switch2 should be connected via a crossover cable.
  Router1 will not play a role in communications between host A and host D.
  The FastEthernet 0/0 interface on Router1 must be configured with subinterfaces.
  Router1 needs more LAN interfaces to accommodate the VLANs that are shown in the exhibit.
  The FastEthernet 0/0 interface on Router1 and the FastEthernet 0/1 interface on Switch2 trunk ports must be configured using the same encapsulation type

## Slide 46: 064
Which two of these are characteristics of the 802.1Q protocol? (Choose two.)
  It is used exclusively for tagging VLAN frames and does not address network reconvergence following switched network topology changes.
  It modifies the 802.3 frame header, and thus requires that the FCS be recomputed.
  It is a Layer 2 messaging protocol which maintains VLAN configurations across networks.
  It includes an 8-bit field which specifies the priority of a frame.
  It is a trunking protocol capable of carrying untagged frames.

## Slide 47: 065
Refer to the exhibit. Each of these four switches has been configured with a hostname, as well as being configured to run RSTP. No other configuration changes have been made. Which three of these show the correct RSTP port roles for the indicated switches and interfaces? (Choose three.)

## Slide 48: 065
  SwitchA, Fa0/2, designated
  SwitchA, Fa0/1, root
  SwitchB, Gi0/2, root
  SwitchB, Gi0/1, designated
  SwitchC, Fa0/2, root
  SwitchD, Gi0/2, root

## Slide 49: 066
Refer to the exhibit. The network administrator normally establishes a Telnet session with the switch from host A. However, host A is unavailable. The administrator's attempt to telnet to the switch from host B fails, but pings to the other two hosts are successful. What is the issue?

## Slide 50: 066
  Host B and the switch need to be in the same subnet.
  The switch interface connected to the router is down.
  Host B needs to be assigned an IP address in VLAN 1.
  The switch needs an appropriate default gateway assigned.
  The switch interfaces need the appropriate IP addresses assigned.

## Slide 51: 067
Refer to the exhibit. Which switch provides the spanning-tree designated port role for the network segment that services the printers?
  Switch1
  Switch2
  Switch3
  Switch4

## Slide 52: 068
What is one benefit of PVST+?
  PVST+ supports Layer 3 load balancing without loops.
  PVST+ reduces the CPU cycles for all the switches in the network.
  PVST+ allows the root switch location to be optimized per VLAN.
  PVST+ automatically selects the root bridge location, to provide optimized bandwidth usage.

## Slide 53: 069
Which are valid modes for a switch port used as a VLAN trunk? (Choose three.)
  transparent
  auto
  on
  desirable
  blocking
  forwarding

## Slide 54: 070
Refer to Exhibit. How many broadcast domains are shown in the graphic assuming only the default VLAN is configured on the switches?
  one
  two
  six
  twelve

## Slide 55: 071
Which three of these statements regarding 802.1Q trunking are correct? (Choose three.)
  802.1Q native VLAN frames are untagged by default.
  802.1Q trunking ports can also be secure ports.
  802.1Q trunks can use 10 Mb/s Ethernet interfaces.
  802.1Q trunks require full-duplex, point-to-point connectivity.
  802.1Q trunks should have native VLANs that are the same at both ends.
Notes: Native VLAN frames are carried over the trunk link untagged -> A is correct.
802.1Q trunking ports carry all the traffic of all VLANs so it cannot be the secure ports. A secure port should be only configured to connect with terminal devices (hosts, printers, servers…) -> B is not correct.
The Inter-Switch Link (ISL) encapsulation requires FastEthernet or greater to operate but 802.1q supports 10Mb/s Ethernet interfaces. -> C is correct.
802.1Q supports point-to-multipoint connectivity. Although in Cisco implementation, a “trunk” is considered a point-to-point link but 802.1q encapsulation can be used on an Ethernet segment shared by more than two devices. Such a configuration is seldom needed but is still possible with the disablement of DTP negotiation. -> D is not correct (Reference:http://www.cisco.com/en/US/products/hw/switches/ps700/products_tech_note09186a008012ecf3.shtml)
The native VLAN that is configured on each end of an 802.1Q trunk must be the same. This is because when a switch receives an untagged frame, it will assign that frame to the native VLAN. If one end is configured VLAN1 as the native VLAN while the other end is configured VLAN2 as the native VLAN, a frame sent in VLAN1 on one side will be received on VLAN2 on the other side -> E is correct.

## Slide 56: 072
Refer to the exhibit. The output that is shown is generated at a switch. Which three statements are true? (Choose three.)

## Slide 57: 072
  All ports will be in a state of discarding, learning, or forwarding.
  Thirty VLANs have been configured on this switch.
  The bridge priority is lower than the default value for spanning tree.
  All interfaces that are shown are on shared media.
  All designated ports are in a forwarding state.
  This switch must be the root bridge for all VLANs on this switch.

## Slide 58: 073
Refer to the exhibit. At the end of an RSTP election process, which access layer switch port will assume the discarding role?
  Switch3, port fa0/1
  Switch3, port fa0/12
  Switch4, port fa0/11
  Switch4, port fa0/2
  Switch3, port Gi0/1
  Switch3, port Gi0/2

## Slide 59: 074
Which term describes a spanning-tree network that has all switch ports in either the blocking or fowarding state?
  converged
  redundant
  provisioned
  spanned

## Slide 60: 075
What are the possible trunking modes for a switch port? (Choose three.)
  transparent
  auto
  on
  desirable
  client
  forwarding

## Slide 61: 076
Which two of these statements regarding RSTP are correct? (Choose two.)
  RSTP cannot operate with PVST+.
  RSTP defines new port roles.
  RSTP defines no new port states.
  RSTP is a proprietary implementation of IEEE 802.1D STP.
  RSTP is compatible with the original IEEE 802.1D STP.

## Slide 62: 077
Refer to the exhibit. Which two statements are true of the interfaces on Switch1? (Choose two.)

## Slide 63: 077
  Multiple devices are connected directly to FastEthernet0/1.
  A hub is connected directly to FastEthernet0/5.
  FastEthernet0/1 is connected to a host with multiple network interface cards.
  FastEthernet0/5 has statically assigned MAC addresses.
  FastEthernet0/1 is configured as a trunk link.
  Interface FastEthernet0/2 has been disabled.

## Slide 64: 078
Three switches are connected to one another via trunk ports. Assuming the default switch configuration, which switch is elected as the root bridge for the spanning-tree instance of VLAN 1?
  the switch with the highest MAC address
  the switch with the lowest MAC address
  the switch with the highest IP address
  the switch with the lowest IP address

## Slide 65: 079
What are three advantages of VLANs? (Choose three.)
  VLANs establish broadcast domains in switched networks.
  VLANs utilize packet filtering to enhance network security.
  VLANs provide a method of conserving IP addresses in large networks.
  VLANs provide a low-latency internetworking alternative to routed networks.
  VLANs allow access to network services based on department, not physical location.
  VLANs can greatly simplify adding, moving, or changing hosts on the network.

## Slide 66: 080
Cisco Catalyst switches CAT1 and CAT2 have a connection between them using ports FA0/13. An 802.1Q trunk is configured between the two switches. On CAT1, VLAN 10 is chosen as native, but on CAT2 the native VLAN is not specified. What will happen in this scenario?
  802.1Q giants frames could saturate the link.
  VLAN 10 on CAT1 and VLAN 1 on CAT2 will send untagged frames.
  A native VLAN mismatch error message will appear.
  VLAN 10 on CAT1 and VLAN 1 on CAT2 will send tagged frames.

## Slide 67: 081
Refer to the exhibit. A network technician is asked to design a small network with redundancy. The exhibit represents this design, with all hosts configured in the same VLAN. What conclusions can be made about this design?

## Slide 68: 081
  This design will function as intended.
  Spanning-tree will need to be used.
  The router will not accept the addressing scheme.
  The connection between switches should be a trunk.
  The router interfaces must be encapsulated with the 802.1Q protocol.

## Slide 69: 082
Refer to the exhibit. A technician is troubleshooting host connectivity issues on the switches. The hosts in VLANs 10 and 15 on Sw11 are unable to communicate with hosts in the same VLANs on Sw12. Hosts in the Admin VLAN are able to communicate. The port-to-VLAN assignments are identical on the two switches. What could be the problem?

## Slide 70: 082
  The Fa0/1 port is not operational on one of the switches.
  The link connecting the switches has not been configured as a trunk.
  At least one port needs to be configured in VLAN 1 for VLANs 10 and 15 to be able to communicate.
  Port FastEthernet 0/1 needs to be configured as an access link on both switches.
  A router is required for hosts on SW11 in VLANs 10 and 15 to communicate with hosts in the same VLAN on Sw12.

## Slide 71: 083
Refer to the exhibit. Given this output for SwitchC, what should the network administrator's next action be?

## Slide 72: 083
  Check the trunk encapsulation mode for SwitchC's fa0/1 port.
  Check the duplex mode for SwitchC's fa0/1 port.
  Check the duplex mode for SwitchA's fa0/2 port.
  Check the trunk encapsulation mode for SwitchA's fa0/2 port.

## Slide 73: Port Aggregation Protocol

## Slide 74: Link Aggregation Control Protocol

## Slide 75: Configuration Guidelines
The following guidelines and restrictions are useful for configuring EtherChannel
  EtherChannel support - All Ethernet interfaces on all modules must support EtherChannel with no requirement that interfaces be physically contiguous, or on the same module.
  Speed and duplex - Configure all interfaces in an EtherChannel to operate at the same speed and in the same duplex mode
  VLAN match - All interfaces in the EtherChannel bundle must be assigned to the same VLAN, or be configured as a trunk
  Range of VLAN - An EtherChannel supports the same allowed range of VLANs on all the interfaces in a trunking EtherChannel. If the allowed range of VLANs is not the same, the interfaces do not form an EtherChannel, even when set to auto or desirable mode
If these settings must be changed, configure them in port channel interface configuration mode
  configurations that are applied to the individual interfaces do not affect the port channel interface

## Slide 76: 084
Refer to the exhibit. A network administrator is configuring an EtherChannel between SW1 and SW2. The SW1 configuration is shown. What is the correct configuration for SW2?

## Slide 77: 084
  interface FastEthernet 0/1
  channel-group 1 mode active
  switchport trunk encapsulation dot1q
  switchport mode trunk
  interface FastEthernet 0/2
  channel-group 1 mode active
  switchport trunk encapsulation dot1q
  switchport mode trunk
  interface FastEthernet 0/1
  channel-group 2 mode auto
  switchport trunk encapsulation dot1q
  switchport mode trunk
  interface FastEthernet 0/2
  channel-group 2 mode auto
  switchport trunk encapsulation dot1q
  switchport mode trunk
  interface FastEthernet 0/1
  channel-group 1 mode desirable
  switchport trunk encapsulation dot1q
  switchport mode trunk
  interface FastEthernet 0/2
  channel-group 1 mode desirable
  switchport trunk encapsulation dot1q
  switchport mode trunk
  interface FastEthernet 0/1
  channel-group 1 mode passive
  switchport trunk encapsulation dot1q
  switchport mode trunk
  interface FastEthernet 0/2
  channel-group 1 mode passive
  switchport trunk encapsulation dot1q
  switchport mode trunk

## Slide 78: 085
What parameter can be different on ports within an EtherChannel?
  speed
  DTP negotiation settings
  trunk encapsulation
  duplex

## Slide 79: 086
Refer to the exhibit. What set of commands was configured on interface Fa0/3 to produce the given output?

## Slide 80: 086
  interface FastEthernet 0/3
  channel-group 1 mode desirable
  switchport trunk encapsulation dot1q
  switchport mode trunk
  interface FastEthernet 0/3
  channel-group 2 mode passive
  switchport trunk encapsulation dot1q
  switchport mode trunk
  interface FastEthernet 0/3
  channel-group 2 mode active
  switchport trunk encapsulation dot1q
  switchport mode trunk
  interface FastEthernet 0/3
  channel-group 2 mode on
  switchport trunk encapsulation dot1q
  switchport mode trunk

## Slide 81: 087
A network administrator creates a layer 3 EtherChannel, bundling four interfaces into channel group 1. On what interface is the IP address configured?
  the port-channel 1 interface
  the highest number member interface
  all member interfaces
  the lowest number member interface