## Slide 1: Topic 3 IP addressing (IPv4 / IPv6)
CCNA Routing and Switching
200-120 Examination
Jeng-Yueng Chen
Hsiuping University of Science and Technology

## Slide 2: 088
You have been asked to come up with a subnet mask that will allow all three web servers to be on the same network while providing the maximum number of subnets. Which network address and subnet mask meet this requirement?
  192.168.252.0 255.255.255.252
  192.168.252.8 255.255.255.248
  192.168.252.8 255.255.255.252
  192.168.252.16 255.255.255.240
  192.168.252.16 255.255.255.252

## Slide 3: 089
Given an IP address 172.16.28.252 with a subnet mask of 255.255.240.0, what is the correct network address?
  172.16.16.0
  172.16.0.0
  172.16.24.0
  172.16.28.0

## Slide 4: 090
Which IPv6 address is the equivalent of the IPv4 interface loopback address 127.0.0.1?
  ::1
  ::
  2000::/3
  0::/10

## Slide 5: 091
You are working in a data center environment and are assigned the address range 10.188.31.0/23. You are asked to develop an IP addressing plan to allow the maximum number of subnets with as many as 30 hosts each. Which IP address range meets these requirements?
  10.188.31.0/26
  10.188.31.0/25
  10.188.31.0/28
  10.188.31.0/27
  10.188.31.0/29

## Slide 6: 092
What are three features of the IPv6 protocol? (Choose three.)
  optional IPsec
  autoconfiguration
  no broadcasts
  complicated header
  plug-and-play
  checksums

## Slide 7: 093
Which command enables IPv6 forwarding on a Cisco router?
  ipv6 local
  ipv6 host
  ipv6 unicast-routing
  ipv6 neighbor

## Slide 8: 094
What is known as "one-to-nearest" addressing in IPv6?
  global unicast
  anycast
  multicast
  unspecified address

## Slide 9: 095
What is the first 24 bits in a MAC address called?
  NIC
  BIA
  OUI
  VAI

## Slide 10: 096
Refer to the exhibit. Which subnet mask will place all hosts on Network B in the same subnet with the least amount of wasted addresses?
  255.255.255.0
  255.255.254.0
  255.255.252.0
  255.255.248.0

## Slide 11: 097
Refer to the exhibit. What is the most appropriate summarization for these routes?
  10.0.0.0 /21
  10.0.0.0 /22
  10.0.0.0 /23
  10.0.0.0 /24

## Slide 12: 098
Which two are features of IPv6? (Choose two.)
  anycast
  broadcast
  multicast
  podcast
  allcast

## Slide 13: 099
Which two of these statements are true of IPv6 address representation? (Choose two.)
  There are four types of IPv6 addresses: unicast, multicast, anycast, and broadcast.
  A single interface may be assigned multiple IPv6 addresses of any type.
  Every IPv6 interface contains at least one loopback address.
  The first 64 bits represent the dynamically created interface ID.
  Leading zeros in an IPv6 16 bit hexadecimal field are mandatory.

## Slide 14: 100
Refer to the exhibit. A new subnet with 60 hosts has been added to the network. Which subnet address should this network use to provide enough usable addresses while wasting the fewest addresses?
  192.168.1.56/26
  192.168.1.56/27
  192.168.1.64/26
  192.168.1.64/27

## Slide 15: 101
Refer to the exhibit. All of the routers in the network are configured with the ip subnet-zero command. Which network addresses should be used for Link A and Network A? (Choose two.)
  Network A - 172.16.3.48/26
  Network A - 172.16.3.128/25
  Network A - 172.16.3.192/26
  Link A - 172.16.3.0/30
  Link A - 172.16.3.40/30
  Link A - 172.16.3.112/30

## Slide 16: 102
The network administrator needs to address seven LANs. RIP version 1 is the only routing protocol in use on the network and subnet 0 is not being used. What is the maximum number of usable IP addresses that can be supported on each LAN if the organization is using one class C address block?
  8
  6
  30
  32
  14
  16

## Slide 17: 103
What will happen if a private IP address is assigned to a public interface connected to an ISP?
  Addresses in a private range will be not be routed on the Internet backbone.
  Only the ISP router will have the capability to access the public network.
  The NAT process will be used to translate this address to a valid IP address.
  A conflict of IP addresses happens, because other public routers can use the same range.

## Slide 18: 104
Which two benefits are provided by using a hierarchical addressing network addressing scheme? (Choose two.)
  reduces routing table entries
  auto-negotiation of media rates
  efficient utilization of MAC addresses
  dedicated communications between devices
  ease of management and troubleshooting

## Slide 19: 105
What is the alternative notation for the IPv6 address B514:82C3:0000:0000:0029:EC7A:0000:EC72?
  B514 : 82C3 : 0029 : EC7A : EC72
  B514 : 82C3 :: 0029 : EC7A : EC72
  B514 : 82C3 : 0029 :: EC7A : 0000 : EC72
  B514 : 82C3 :: 0029 : EC7A : 0 : EC72

## Slide 20: 106
Refer to the diagram. All hosts have connectivity with one another. Which statements describe the addressing scheme that is in use in the network? (Choose three.)

## Slide 21: 106
  The subnet mask in use is 255.255.255.192.
  The subnet mask in use is 255.255.255.128.
  The IP address 172.16.1.25 can be assigned to hosts in VLAN1
  The IP address 172.16.1.205 can be assigned to hosts in VLAN1
  The LAN interface of the router is configured with one IP address.
  The LAN interface of the router is configured with multiple IP addresses.

## Slide 22: 107
Which two statements describe characteristics of IPv6 unicast addressing? (Choose two.)
  Global addresses start with 2000::/3.
  Link-local addresses start with FE00:/12.
  Link-local addresses start with FF00::/10.
  There is only one loopback address and it is ::1.
  If a global address is assigned to an interface, then that is the only allowable address for the interface.

## Slide 23: 108
The network administrator has been asked to give reasons for moving from IPv4 to IPv6. What are two valid reasons for adopting IPv6 over IPv4? (Choose two.)
  no broadcast
  change of source address in the IPv6 header
  change of destination address in the IPv6 header
  Telnet access does not require a password
  autoconfiguration
  NAT

## Slide 24: 109
An administrator must assign static IP addresses to the servers in a network. For network 192.168.20.24/29, the router is assigned the first usable host address while the sales server is given the last usable host address. Which of the following should be entered into the IP properties box for the sales server?
  IP address: 192.168.20.14
  Subnet Mask: 255.255.255.248
  Default Gateway: 192.168.20.9
  IP address: 192.168.20.254
  Subnet Mask: 255.255.255.0
  Default Gateway: 192.168.20.1
  IP address: 192.168.20.30
  Subnet Mask: 255.255.255.248
  Default Gateway: 192.168.20.25
  IP address: 192.168.20.30
  Subnet Mask: 255.255.255.240
  Default Gateway: 192.168.20.17
  IP address: 192.168.20.30
  Subnet Mask: 255.255.255.240
  Default Gateway: 192.168.20.25

## Slide 25: 110
Which subnet mask would be appropriate for a network address range to be subnetted for up to eight LANs, with each LAN containing 5 to 26 hosts?
  0.0.0.240
  255.255.255.252
  255.255.255.0
  255.255.255.224
  255.255.255.240

## Slide 26: 111
How many bits are contained in each field of an IPv6 address?
  24
  4
  8
  16

## Slide 27: 112
What are three approaches that are used when migrating from an IPv4 addressing scheme to an IPv6 scheme. (Choose three.)
  enable dual-stack routing
  configure IPv6 directly
  configure IPv4 tunnels between IPv6 islands
  use proxying and translation to translate IPv6 packets into IPv4 packets
  statically map IPv4 addresses to IPv6 addresses
  use DHCPv6 to map IPv4 addresses to IPv6 addresses

## Slide 28: 113
Refer to the exhibit. In this VLSM addressing scheme, what summary address would be sent from router A?
  172.16.0.0 /16
  172.16.0.0 /20
  172.16.0.0 /24
  172.32.0.0 /16
  172.32.0.0 /17
  172.64.0.0 /16

## Slide 29: 114
How is an EUI-64 format interface ID created from a 48-bit MAC address?
  by appending 0xFF to the MAC address
  by prefixing the MAC address with 0xFFEE
  by prefixing the MAC address with 0xFF and appending 0xFF to it
  by inserting 0xFFFE between the upper three bytes and the lower three bytes of the MAC address
  by prefixing the MAC address with 0xF and inserting 0xF after each of its first three bytes

## Slide 30: 115
Refer to the exhibit. What is the most efficient summarization that R1 can use to advertise its networks to R2?
  172.1.0.0/22
  172.1.0.0/21
  172.1.4.0/22
  172.1.4.0/24
  172.1.5.0/24
  172.1.6.0/24
  172.1.7.0/24
  172.1.4.0/25
  172.1.4.128/25
  172.1.5.0/24
  172.1.6.0/24
  172.1.7.0/24

## Slide 31: 116
Which option is a valid IPv6 address?
  2001:0000:130F::099a::12a
  2002:7654:A1AD:61:81AF:CCC1
  FEC0:ABCD:WXYZ:0067::2A4
  2004:1:25A4:886F::1

## Slide 32: 117
Which three are characteristics of an IPv6 anycast address? (Choose three.)
  one-to-many communication model
  one-to-nearest communication model
  any-to-many communication model
  a unique IPv6 address for each device in the group
  the same address for multiple devices in the group
  delivery of packets to the group interface that is closest to the sending device

## Slide 33: 118
A national retail chain needs to design an IP addressing scheme to support a nationwide network. The company needs a minimum of 300 sub-networks and a maximum of 50 host addresses per subnet. Working with only one Class B address, which of the following subnet masks will support an appropriate addressing scheme? (Choose two.)
  255.255.255.0
  255.255.255.128
  255.255.252.0
  255.255.255.224
  255.255.255.192
  255.255.248.0

## Slide 34: 119
Refer to the exhibit. A network administrator is adding two new hosts to SwitchA. Which three values could be used for the configuration of these hosts? (Choose three.)

## Slide 35: 119
  host A IP address: 192.168.1.79
  host A IP address: 192.168.1.64
  host A default gateway: 192.168.1.78
  host B IP address: 192.168.1.128
  host B default gateway: 192.168.1.129
  host B IP address: 192.168.1.190

## Slide 36: 120
Which IPv6 address is the all-router multicast group?
  FF02::1
  FF02::2
  FF02::3
  FF02::4
Notes: FF02::1 All Nodes
FF02::2 All Routers
FF02::4 DVMRP Routers
FF02::5 OSPF
FF02::6 OSPF DR
FF02::9 RIP Routers
FF02::A EIGRP Routers

## Slide 37: 121
Refer to the exhibit. Which address range efficiently summarizes the routing table of the addresses for router Main?
  172.16.0.0./21
  172.16.0.0./20
  172.16.0.0./16
  172.16.0.0/18

## Slide 38: 122
Which IPv6 address is valid?
  2001:0db8:0000:130F:0000:0000:08GC:140B
  2001:0db8:0:130H::87C:140B
  2031::130F::9C0:876A:130B
  2031:0:130F::9C0:876A:130B

## Slide 39: 123
Which command can you use to manually assign a static IPv6 address to a router interface?
  ipv6 autoconfig 2001:db8:2222:7272::72/64
  ipv6 address 2001:db8:2222:7272::72/64
  ipv6 address PREFIX_1 ::1/64
  ipv6 autoconfig

## Slide 40: 124
Which of these represents an IPv6 link-local address?
  FE80::380e:611a:e14f:3d69
  FE81::280f:512b:e14f:3d69
  FEFE:0345:5f1b::e14d:3d69
  FE08::280e:611:a:f14f:3d69
Notes: FE80::/10 has been reserved for link-local unicast addressing
The actual link local addresses are assigned with the prefix FE80::/64

## Slide 41: 125
The network administrator is asked to configure 113 point-to-point links. Which IP addressing scheme defines the address range and subnet mask that meet the requirement and waste the fewest subnet and host addresses?
  10.10.0.0/16 subnetted with mask 255.255.255.252
  10.10.0.0/18 subnetted with mask 255.255.255.252
  10.10.1.0/24 subnetted with mask 255.255.255.252
  10.10.0.0/23 subnetted with mask 255.255.255.252
  10.10.1.0/25 subnetted with mask 255.255.255.252